## Slide 1
LitDP-413B Fiber Distribution Box
Max. 24F splicing, 16F termination
LitDP-413B is a subscriber optical fiber access box that is used to build FTTH network. It is designed to provide a protected access point between the distribution cable and drop cable. Splitter is pre-installed in the box.
Features
Beautiful and compact model, convenient installation
Nontoxic material, non-corrosive metal components
Compatible with different optical cables
Neat fiber routing management
Application
Outdoor application
Wall, or pole mounting scenarios

## Slide 2
Specifications
Item | Specification
Dimension (H × W × D) | 237.5mm × 204mm × 77mm (±5mm)
Splice capacity | Max. 24F
Number of adapters | Max. 16 SC adapters
Configurable splitter | 2 × 1:8 or 1 × 1:16 micro-type splitter
Distribution cable port | A pair of mid-span cables: Φ6-14mm; one branch cable: Φ6-14mm
Drop cable port | 16 drop cables: 2×3mm
Product Details
Box cover
Bottom case
Turnover board
Splitter holder
Adapter
237.5mm
204mm
77mm
Mid-span cable port
Branch cable port
Drop cable port

## Slide 3
Fiber Route
Mid-span cable (uncut)
Mid-span cable (stripped)
Splitter input
Splitter output
Drop cable with the field installable connector
Standard Accessories |  |  | 
No. | Name | Picture | Quantity
1 | Hose clamp |  | 3 pcs
2 | Fiber splice protective sleeve |  | 17 pcs
3 | Nylon cable tie |  | 5 pcs
4 | Drop cable clip |  | 2 set (for 16 drop cables）
5 | Bare fiber protective sleeve |  | 0.5m
6 | Resealable bag |  | 1 pc
7 | Wall mounting kit |  | 1 set
Accessory List

## Slide 4
Optional Accessories |  |  | 
No. | Name | Picture | Quantity
1 | Pole mounting kit |  | 1 set