## Slide 1
LitJTP-180J-A104-V304 Dome-Base Closure
Mechanical sealing, 144F splicing
LitJTP-180J series are dome-base closures with mechanical sealing, which are designed for all cable application environments such as duct, aerial, and man-hole. LitJTP supports numerous functions as mid-span, branch and direct splice. The closure is accommodated with flexible splice trays and various accessories are available for many scenarios. Rigorous tests are performed to approve the best quality for network reliability.
Features
Dome-base design structure with mechanical sealing
High-strength modified polypropylene material
Mid-span operation without cutting the cable
Flexible grommets for universal standardized cables
Ideal fiber management design
Application
Outdoor application
Wall, pole, wire mounting scenarios

## Slide 2
Specifications
Item | LitJTP-180J-A104-V304
Dimension | Φ180mm × 445mm (±5mm)
Oval hole diameter | Φ10-18mm
Round hole diameter | Φ8-14mm
Splice tray capacity (single fiber) | 36F
Number of splice tray | 4 pcs (NO. V3 splice tray)
Splicing capacity (single fiber) | 144F
Sealing mode | Mechanical sealing
Color | Black
Product Details
Latch
Dome shell
Base
Splice tray
D = 180mm; D1 = 130mm; D2 = 160mm; L = 445mm
L
D1
D2
D
Sealing ring
Fixing platform
1 oval hole
4 round holes

## Slide 3
Item | NO. V3 splice tray
Function | Fiber splice and storage
Dimension | 240mm × 110mm × 10mm
Splice capacity (single fiber) | 36F
Product photo | 
Splice Tray
Accessory List
Standard Accessories |  |  | 
No. | Name | Picture | Quantity
1 | Fiber splice protective sleeve |  | 144 pcs
2 | Nylon cable tie |  | 16 pcs
3 | Bare fiber protective sleeve |  | 3m
4 | Branch clamp nut |  | 4 pcs
5 | Φ10-14mm sealing plug (for branch cable) |  | 4 pcs

## Slide 4
6 | Wrench for branch clamp nut |  | 1 pc
7 | Allen key |  | 1 pc
8 | Φ10-14mm double-hole sealing plug (for mid-span cable) |  | 1 pc
9 | Insulation tape |  | 2m
10 | Wall mounting kit |  | 1 set (2 brackets, 2 M5 screws, 2 M5 hex nuts, 2 self-tapping screws, 2 plastic expansion sleeves)
Optional Accessories |  |  | 
No. | Name | Picture | Quantity
1 | Φ14-18mm double-hole sealing plug (for mid-span cable) |  | 1 pc
2 | Pole mounting kit |  | 1 set (2 pole hoops)
3 | Wire mounting kit |  | 1 set (2 hooks)